## Slide 1
ML PERFORMANCE | LOCKED SYNTHETIC TEST
Technical feasibility · SIH 2026
CLASSIFIER · TUNED XGBOOST
9.33%
Critical recall
ALERT ENGINE · SYSTEM LEVEL
−3.33 h
Median lead time
Model comparison
Classification and operational rates from the same locked synthetic test
Model | Critical recall | Macro PR-AUC | Macro F1 | Normal false-alarm rate | p50 latency | p95 latency | Sample memory
Tuned XGBoost | 9.33% | 0.503 | 0.446 | 15.08% | 0.317 ms | 0.613 ms | 550.625 MiB
Default XGBoost | 4.57% | 0.535 | 0.445 | 3.72% | Not measured | Not measured | Not measured
Logistic Regression | 76.50% | 0.469 | 0.430 | 62.63% | Not measured | Not measured | Not measured
Threshold Rule | 4.16% | 0.415 | 0.390 | 1.74% | Not measured | Not measured | Not measured
Critical recall and normal false-alarm rate
Classifier-level rates · percent of respective class
Chart: 
| Tuned XGBoost | Default XGBoost | Logistic Regression | Threshold Rule
Critical recall | 0.093333 | 0.045689 | 0.76498 | 0.0416
Normal false-alarm rate | 0.15076 | 0.037156 | 0.62631 | 0.017422
Alert engine · system level
Separate from classifier-level rates
Median lead time | −3.333 h
P10 lead time | −11.667 h
False alerts per normal event-day | 0.046 episodes/day
CALIBRATION · Locked-test calibration: Not measured
Synthetic evaluation only. Useful early-warning performance and real-mine transfer remain unverified.
Notes: Sources: reports/final_eval.json (locked synthetic test risk models and alert engine); reports/tuning/robustness.json (tuned XGBoost workstation CPU p50/p95 latency and sampled RSS). Other model profiling and locked-test calibration were not measured. Display values rounded only.